## Slide 1
Car Cab Air Quality in Rush Hour Traffic
Department of Mechanical Engineering
University of Colorado, Boulder
Conclusions
For best air quality, drive with the windows open if the weather is faborable, even in traffic
Use HVAC if the weather is bad – better than no ventilation
HVAC may be cycling on in the background even if it is turned off
Corey Trujillo
Background & Motivation
Humans consume oxygen when inhaling, produce carbon dioxide (CO2) and water when exhaling and generate heat as a product of metabolic processes.[1] Automobiles expel water, CO2, carbon monoxide, volatile organic compounds (VOCs) in their exhaust.[2] Carbon dioxide can cause lethargy, headache and nausea[3] while carbon monoxide can lead to death.[4] This study examines different methods of ventilation.
Methodology
Temperature, relative humidity, CO2 and VOCs were measured in the cab of a 2003 GMC Envoy with three adult passengers in three different ventilation scenarios (Table 1). The 13 mile loop was completed three times in rush hour traffic with a stop for fuel.
Acknowledgements
Thanks to Taylor Maxwell and Lauren Shurnas for helping me complete this experiment. Thanks to Dr. Daniel Knight, Dr. Michael Hannigan and Rachel Moore for their instruction and support through this course and thanks to the Hannigan Lab for lending us their air quality sensors. This would not have been possible without each of you!
References
[1]https://www.bbc.com/bitesize/guides/zw9x8mn/revision/7
[2]S. R. Turns, An Introduction to Combustion: Concepts and Applications. New York: McGraw-Hill, 2012. OCLC: 660161844.
[3]http://www.health.state.mn.us/divs/eh/in
doorair/co2/index.html
[4]https://www.slideshare.net/frankdispenza/carbon-monoxide-14870187
Results
Windows open led to lowest measured values
Highest measured values were seen with AC off and windows closed
HVAC works, but not as well as windows
Data Limitations
Only one POD used (no comparison)
Data were lost from 5:15 to 5:25 pm, likely due to an electrical failure.
Discussion
The car was best ventilated with windows open and worst with HVAC off and windows closed. Unexpectedly, the data oscillates. Possible causes for this could be the HVAC system still might operate cyclically while off, ventilating the cab. Another interesting feature of the data is the peak in light VOCs during the first loop. This could be due to one of the passengers eating pizza.
Figure 2: Carbon Dioxide and VOCs
Figure 3: Relative Humidity and Temperature
Table 1: Experiment Itinerary
Figure 1: POD Air Quality Monitor