## Slide 1
What’s In Our Stars? Student Procedures

## Slide 2: Computer Prep 1. Equipment Prep 2. Data Collection 3. Post-Lab 4.
Installing and preparing the computer application
Setting up the lab equipment and samples
Running the experiment and collecting data
Interpreting and analyzing the data collected

## Slide 3: 1. Computer Prep
Follow these steps to install the needed programs on your device.

## Slide 4: ARDUINO IDE – DOWNLOAD/INSTALL
1. Go to https://www.arduino.cc/en/software and select the software that is appropriate for your student device.
2. Follow the installation prompts.
3. If asked for an admin username and password, raise your hand and your teacher will come to you.
Notes: Image Source – Abbott (Self)

## Slide 5: SPARKFUN LIBRARY
1. Once installed, open Arduino IDE.
2. Click on the books icon on the task bar located on the left-hand side.
Notes: Image Source – Abbott (Self)

## Slide 6: SPARKFUN LIBRARY (cont.)
3. Type “SparkFun Spectral Triad” into the search bar.
4. Select Install.
Notes: Image Source – Abbott (Self)

## Slide 7: 1. Google Classroom 2. Select 3. Open ACTIVITY CODE
Go to the assignment posted in Google classroom.
Click on the attachment labeled “Whats_In_Our_Stars_Arduino_Code.”
Select the option at the top that says “Open with Arduino IDE.”
4. OK!
Click “Okay.”
(This just creates a file within the Arduino sketchbook.)
Notes: Image Sources – Abbott (Self)

## Slide 8: EXCEL DATA STREAMER
Open Microsoft Excel. (You may have to type it into your Windows search bar.)
Go to File > Options > Add-Ins.
Make sure COM Add-ins is selected in the Manage box and click Go.
In the COM add-Ins dialog box, make sure to select the box next to Microsoft Data Streamer for Excel add-in, then click OK.
Video Source: Microsoft Support LINK
Notes: Video Source – Microsoft Support LINK

## Slide 9: 1. Google Classroom 2. Select 3. New Window DATA DASHBOARD
Go to the assignment posted in Google classroom.
Click on the attachment labeled “Whats_In_Our_Stars_Data_Dashboard.”
Select the three dots in the upper right-hand corner and then click “Open in new window.”
4. Open
When the new window loads, select “Open with Excel” at the top of the screen.
Notes: Image Sources – Abbott (Self)

## Slide 10: 2. Equipment Prep
This section includes procedures for wiring/hooking up the spectrometer.

## Slide 11: SPECTROMETER SETUP
SparkFun Triad Spectroscopy Sensor
SparkFun 4-pin Qwiic connect cable (or 4 jumper cables)
Arduino Uno Board
USB-C to USB-A cable
Black cardstock or thin cardboard cut into a 3”x 3” square
Scissors
Notes: Image Sources:
Sensor – Abbott (Self)
Arduino – Abbott (Self)
Qwiic cables – Abbott (Self)
USB cable – “Cable USB” by Mariofergo Wikimedia Commons licensed under CC BY-SA 4.0 – link in picture
Scissors – “A pair of large Fiskars scissors, molded for right hands.” by Evan-amos Wikimedia Commons licensed under Public Domain – link in picture

## Slide 12: SPECTROMETER SETUP
Black = GND
Red = 3.3V
Blue = SDA
Yellow = SCL
Connect the triad sensor to the Arduino, making sure that each colored cable goes to the correct pin!
(see above)
Notes: Image Sources:
Arduino – TinkerCad
SparkFun Sensor – Abbott (Self)

## Slide 13: SPECTROMETER SETUP
Black = GND
Red = 3.3V
Blue = SDA
Yellow = SCL
Connect the triad sensor to the Arduino, making sure that each colored cable goes to the correct pin!
(see above)
Notes: Image Sources:
SparkFun Sensor to Arduino Uno Qwiic cable connection – Abbott (Self)

## Slide 14: SPECTROMETER SETUP
Use the provided USB cable to connect the spectrometer to your device.
Notes: Image Sources:
Computer – “Black laptop computer open frontal” by OpenClipart-Vectors from Wikimedia Commons licensed under CC0 1.0 – link in picture
Arduino Uno Board – TinkerCad

## Slide 15: SAMPLES SETUP
Grab one cup of each substance and one unknown for your group to have a set of 4 samples.
KNOWN A
KNOWN B
KNOWN C
UNKNOWN
(A/B/C)
The name of the substance will be on each sample cup.
(e.g., Iron Filings)
Notes: Image Source – Abbott (Self)

## Slide 16: SAMPLE SETUP
Once you have your spectrometer set up, and your samples selected and portioned into containers, you’ll need to create a “cover” to place over the sample cup for the sensor to sit on and to eliminate ambient light.
8 cm (~3”)
8 cm (~3”)
Cut a piece of black cardstock into a square that will hang over the edges of the sample cups.
Fold the square in half.
Cut out a rectangle from the middle.
3.5 cm (~1.25”)
2 cm (~0.75”)
3.5 cm (~1.25”)
4 cm (~1.5”)

## Slide 17: COMPLETE SETUP
When your setup is complete, it should look like this:
Notes: Image Source – Abbott (Self)

## Slide 18: 3. Data Collection
Part 3 describes how to conduct the experiment and collect data on “lab day.”

## Slide 19: DATA COLLECTION – Part 1: Arduino IDE
1. Select your device from the dropdown menu.
2. Verify the sketch code.
3. Upload the code to the Arduino.
Notes: Image Source – Abbott (Self)

## Slide 20: DATA COLLECTION – Part 2: Excel Dashboard
1. Select “Data Streamer” from the top menu bar.
2. Select “Connect a Device” from the top menu bar, then “Arduino.”
3. Select the “Settings” Sheet from the bottom menu and make sure “Data channels” is set to 18.
Notes: Image Source (All) – Abbott (Self)

## Slide 21: DATA COLLECTION – Part 3: Check Dashboard Data Table
The table on the first sheet should look like the one to the right. 
If it does, you are good to go! You can skip to Slide 25.
If you have any of the “Average Intensity” cells showing the error “#REF”, follow the directions on the next slide.
Notes: Image Source – Abbott (Self)

## Slide 22: DATA COLLECTION – *Part 3A: Dashboard Data Table TROUBLESHOOTING
The error “#REF” indicates that the reference cells for the formula are not found, but the good news is, it’s an easy fix!
Click on the Average Intensity for 410nm.
Type the following formula into the cell: =AVERAGE(TBL_HST[CH1])
Notes: Image Source – Abbott (Self)

## Slide 23: DATA COLLECTION – *Part 3A: Dashboard Data Table TROUBLESHOOTING
4. Each cell formula going down the column should increase by 1 channel.
5. See the table to the right for the correct formulas for Average Intensity at each wavelength.
6. You can copy and paste the formulas for each wavelength from the next slide!
Notes: Image Source – Abbott (Self)

## Slide 24: DATA COLLECTION – *Part 3A: Dashboard Data Table TROUBLESHOOTING
Click on the text box to the right ,
Select all the text, then copy, and paste!
=AVERAGE(TBL_HST[CH1])
=AVERAGE(TBL_HST[CH2])
=AVERAGE(TBL_HST[CH3])
=AVERAGE(TBL_HST[CH4])
=AVERAGE(TBL_HST[CH5])
=AVERAGE(TBL_HST[CH6])
=AVERAGE(TBL_HST[CH7])
=AVERAGE(TBL_HST[CH8])
=AVERAGE(TBL_HST[CH9])
=AVERAGE(TBL_HST[CH10])
=AVERAGE(TBL_HST[CH11])
=AVERAGE(TBL_HST[CH12])
=AVERAGE(TBL_HST[CH13])
=AVERAGE(TBL_HST[CH14])
=AVERAGE(TBL_HST[CH15])
=AVERAGE(TBL_HST[CH16])
=AVERAGE(TBL_HST[CH17])
=AVERAGE(TBL_HST[CH18])

## Slide 25: DATA COLLECTION – Part 4: Start Data
4. On the Dashboard Sheet, select the substance name from the dropdown menu.
5. Click “Start Data” from the Data Streamer menu bar.
6. Click on the “Data Out” Sheet from the bottom menu.
Then type “GO” into cell A5 and hit Enter.
Notes: Image Source (All) – Abbott (Self)

## Slide 26: DATA COLLECTION – Part 5: Collect Data
Return to the Dashboard Sheet using the menu at the bottom of the screen. You should now see values in the data table for average intensity, a bar graph, and a line graph created for you.
Once the values have stabilized (~10 seconds), click “Stop Data” toward the top of the screen.
Notes: Image Source – Abbott (Self)

## Slide 27: DATA COLLECTION – Part 6: Save Data
OPTION #1: Select “File” then “Save As.”
Suggestion: Save files using the following pattern:
“ClassPeriod_Group#_SameName”
“ClassPeriod_GroupInitials_SameName”
e.g., “Hr1_ABC_TableSalt”
OPTION #2: Select “Capture Screen”
Within the Data Streamer menu is “capture screen”; this creates an image of the sheet shown that students can save.
OPTION #3: Use the “Print Screen” shortcut.
Using this keyboard shortcut does the same thing as screen capture above, but automatically saves the image to your “screenshots” folder.
Notes: Image Source (All) – Abbott (Self)

## Slide 28: DATA COLLECTION – Part 7: Record Data
Identify the wavelength values where “peaks” occur on the line graph (see left).
On the student worksheet, use a black marker to draw lines on the provided spectrum at each of the wavelengths where a peak occurred.
Notes: Image Source (All) – Abbott (Self)

## Slide 29: DATA COLLECTION – Part 8: Reset Data
1. Select the next substance to be sampled from the dropdown menu on the dashboard.
3. Press the reset button on the Arduino.
2. Click on the “Reset Data” icon under the data streamer menu.
Notes: Image Source (All) – Abbott (Self)

## Slide 30: DATA COLLECTION – Part 9: Repeat
Repeat the steps to collect data for each of the known samples and the unknown sample.
KNOWN A
KNOWN B
KNOWN C
UNKNOWN
Notes: Image Source (All) – Abbott (Self)

## Slide 31
4. Post Lab
Final steps of the lab activity are provided in this section, including how to analyze the data collected and identify the unknown substance.

## Slide 32: DATA ANALYSIS
Once data and graphs are collected for the 3 known samples and 1 unknown, compare the unknown graph and spectrum to the knowns to identify the sample.
KNOWN B
KNOWN C
KNOWN A
UNKNOWN
MATCH!
Notes: Image Source (All) – Abbott (Self)

## Slide 33: COMPLETE STUDENT HANDOUT
After identifying the unknown substance, complete the analysis questions on the student handout.
Notes: Image Source (All) – Abbott (Self)

## Slide 34: Sources
Kramida, A., Ralchenko, Yu., Reader, J. and NIST ASD Team (2022). NIST Atomic Spectra Database (version 5.10), [Online]. Available: https://physics.nist.gov/asd. National Institute of Standards and Technology, Gaithersburg, MD. DOI: https://doi.org/10.18434/T4W30F
Seidle, Nathan (Nate). Spectral Triad (AS7265x) Hookup Guide, [Online]. Available: https://learn.sparkfun.com/tutorials/spectral-triad-as7265x-hookup-guide?_ga=2.208195537.274963032.1659022095-1771007873.1658366162. SparkFun Electronics. Licensed by CC BY-SA 4.0

## Slide 35: STUDENT HANDOUT spEctrA DIAGRAM
410 nm
435 nm
460 nm
485 nm
510 nm
535 nm
560 nm
585 nm
610 nm
645 nm
680 nm
705 nm
730 nm
760 nm
810 nm
860 nm
900 nm
940 nm
WAVELENGTH