## Slide 1: What’s In Our Stars?
TEACHER PROCEDURES

## Slide 2
What’s In Our Stars? Teacher Procedures

## Slide 3: 1. Computer Prep 2. Equipment Prep 3. Data Collection 4. Post-Lab
Installing and preparing the computer application
Setting up the lab equipment and samples
Running the experiment and collecting data
Interpreting and analyzing the data collected

## Slide 4: —Another Teacher
Dear Teacher:
Spectroscopy is a topic that can be as simple
or as complex as one makes it. In developing this activity, I have been sucked into its “black hole” (pun intended…) many times. I would begin by looking up the absorption spectra of hydrogen and before long I was converting the wavenumbers of bond stretching at a specific wavelength for aldehydes! You know your students best but, to paraphrase the U.S. Navy, my advice would be: Keep It Super Simple! (K.I.S.S.).

## Slide 5: 1. Computer Prep
This section covers the software applications used by students to complete this activity.
I recommend familiarizing yourself with these steps before going through with students.
Additionally, for the sake of time, I would have students complete these steps in class the day prior to conducting the activity.

## Slide 6: ARDUINO IDE
1. Go to https://www.arduino.cc/en/software and select the software that is appropriate for your students’ devices.
2. Have students download and install the software program.
3. Alternatively, students may use the web-based version also accessed using the link above.
Notes: Image Source– Abbott (Self)

## Slide 7: SPARKFUN LIBRARY
1. Once installed, open Arduino IDE.
2. Click on the books icon on the task bar located on the left-hand side.
Notes: Image Source (All) – Abbott (Self)

## Slide 8: SPARKFUN LIBRARY (cont.)
3. Type in “SparkFun Spectral Triad” into the search bar.
4. Select Install.
Specifics about the Spectral Triad AS7265X library commands can be found at this LINK (scroll down about 2/3 of the page to “AS7265x Arduino Library Overview”).
Notes: Image Source (All) – Abbott (Self)

## Slide 9: 2. Open 3. Locate ACTIVITY CODE 1. File
Select “Open” from the dropdown menu.
Locate the file for the code: “Whats_In_Our
_Stars_Arduino_Code”.
(be sure you have unzipped the activity folder first)
Click on “File” in the upper left-hand corner.
4. Open
Select “Open” in the bottom right- hand corner.
*Be sure that you and your students have already downloaded the code to a chosen location (e.g., desktop).
Notes: Image Source (All) – Abbott (Self)

## Slide 10
EXCEL
Ensure that students have access to Microsoft Excel before proceeding.
Locate and open the Excel workbook “Whats_In_Our_Stars_Excel_Dashboard” provided with the activity files.
DATA STREAMER
Download and Enable the Data Streamer add-in for Microsoft Excel. See Microsoft’s “How To” HERE.
DASHBOARD
Notes: Image Source (All) – Abbott (Self)

## Slide 11: 2. Equipment Prep
This section includes procedures for wiring/hooking up the spectrometer and preparing the samples.

## Slide 12: SPECTROMETER SETUP
SparkFun Triad Spectroscopy Sensor
SparkFun 4-pin Qwiic connect cable (or 4 jumper cables)
Arduino Uno Board
USB-C to USB-A cable
Black cardstock or thin cardboard cut into a 3”x 3” square
Scissors
SparkFun Triad Spectroscopy Sensor
SparkFun 4-pin Qwiic connect cable (or 4 jumper cables)
Arduino Uno Board
USB-C to USB-A cable
Black cardstock or thin cardboard cut into a 3”x 3” square
Scissors
Notes: Image Sources:
Sensor – Abbott (Self)
Arduino – Abbott (Self)
Qwiic cables – Abbott (Self)
USB cable – “Cable USB” by Mariofergo Wikimedia Commons licensed under CC BY-SA 4.0 – link in picture
Scissors – “A pair of large Fiskars scissors, molded for right hands.” by Evan-amos Wikimedia Commons licensed under Public Domain – link in picture

## Slide 13: SPECTROMETER SETUP
Black = GND
Red = 3.3V
Blue = SDA
Yellow = SCL
Connect the triad sensor to the Arduino, making sure that each colored cable goes to the correct pin!
(see above)
Notes: Image Sources:
Arduino – TinkerCad
SparkFun Sensor – Abbott (Self)

## Slide 14: SPECTROMETER SETUP
Black = GND
Red = 3.3V
Blue = SDA
Yellow = SCL
Connect the triad sensor to the Arduino, making sure that each colored cable goes to the correct pin!
(see above)
Notes: Image Sources:
SparkFun Sensor to Arduino Uno Qwiic cable connection – Abbott (Self)

## Slide 15: SPECTROMETER SETUP
Use the provided USB cable to connect the spectrometer to your device.
Notes: Image Sources:
Computer – “Black laptop computer open frontal” by OpenClipart-Vectors from Wikimedia Commons licensed under CC0 1.0 – link in picture
Arduino Uno Board – TinkerCad

## Slide 16: SAMPLE PREPARATION
Select 3* different substances for students to use as their samples.
Some Helpful Hints:
Materials may be solids or liquids, though for ease I recommend choosing either 3 solids or 3 liquids.
When/if choosing 3 solid substances, try to choose ones that look similar with the naked eye (e.g., table salt, Epsom salt, and sugar).
Ideally, sample substances would be made from elements hydrogen (Z= 1) to iron (Z=26), as these elements are formed due to fusion within stars.
Some suggestions are listed on the following slide, but feel free to use anything you like!
A “Sample Tracker” document is provided for you to use if you wish : )
*You can always do more than 3 substances per group! However, this will add prep time, supplies needed, and time to complete the lab.

## Slide 17: SAMPLE PREPARATION
Table Salt (NaCl)
Baking Soda (NaHCO3)
Potassium Nitrate (KNO3)
Vinegar/Acetic Acid (CH3COOH)
Table Sugar/Sucrose (C12H22O12)
Aluminum Foil (Al)
Epsom Salt (MgSO4)
Cornstarch (C6H10O5)
Pencil Lead/Graphite (C)
Play Sand (SiO2)
Hydrofluoric Acid - any molarity (HF)
Phosphoric Acid - any molarity (H3PO4)
Chalk/Calcium Carbonate (CaCO3)
Iron Filings (Fe)
Magnesium Ribbon (Mg)
Vegetable Oil (C18H34O2)
Ideas for the 3 different substances to use as samples.
When/if choosing 3 solid substances, try to choose ones that look similar with the naked eye (e.g., table salt, Epsom salt, and sugar).

## Slide 18: SAMPLE PREPARATION
Once you have your selected substances, place them into containers such as those shown below.
Create enough cups of each chosen sample substance for each group to have one set.
}
Number of
Lab Groups
X
Make sure that the substance labeled “Unknown” is the same as either known A, B, or C! Otherwise, students won’t be able to identify it!
Write the name of the substance on each sample cup.
(e.g., Iron Filings)
KNOWN A
KNOWN B
KNOWN C
UNKNOWN
(A/B/C)
Notes: Image Source (All) – Abbott (Self)

## Slide 19: SAMPLE PREPARATION - EXAMPLE
Remember to create enough cups of each sample substance for each group to have one full set.
Use the “sample tracker” to assist in organizing which substance is “A,” “B,” and “C.”
Table Salt
NaCl
Epsom Salt
MgSO4
Sucrose
C12H22O12
UNKNOWN -
A
A
B
C
Notes: Image Source
Sample Cups – Abbott (Self)
Salt Shaker – “Salt shaker on white background” by Dubravko Soric from Wikimedia Commons licensed under CC BY 2.0 – Link in Picture
Sugar – Abbott (Self)
Epsom Salt - Abbott (Self)

## Slide 20: SAMPLE SETUP
Once you have your spectrometer set up, and your samples selected and portioned into containers, you’ll need to create a “cover” to place over the sample cup for the sensor to sit on and to eliminate ambient light.
8 cm (~3”)
8 cm (~3”)
Cut a piece of black cardstock into a square that will hang over the edges of the sample cups.
Fold the square in half.
Cut out a rectangle from the middle.
3.5 cm (~1.25”)
2 cm (~0.75”)
3.5 cm (~1.25”)
4 cm (~1.5”)

## Slide 21: COMPLETE SETUP
Once you have your spectrometer set up, and your samples selected and portioned into containers for student use, the setup should look like the image below:
Notes: Image Source - Abbott (Self)

## Slide 22: 3. Data Collection
Part 3 describes how to conduct the experiment and collect data on “lab day.”

## Slide 23: DATA COLLECTION – Part 1: Arduino IDE
1. Select your device from the dropdown menu.
2. Verify the sketch code.
3. Upload the code to the Arduino.
Notes: Image Source (All) – Abbott (Self)

## Slide 24: DATA COLLECTION – Part 2: Excel Dashboard
1. Select “Data Streamer” from the top menu bar.
2. Select “Connect a Device” from the top menu bar, then “Arduino.”
3. Select the “Settings” Sheet from the bottom menu and make sure “Data channels” is set to 18.
Notes: Image Source (All) – Abbott (Self)

## Slide 25: DATA COLLECTION – Part 3: Check Dashboard Data Table
The table on the first sheet should look like the one to the right. 
If it does, you are good to go! You can skip to Slide 29.
If you have any of the “Average Intensity” cells showing the error “#REF”, follow the directions on the next slide.
Notes: Image Source – Abbott (Self)

## Slide 26: DATA COLLECTION – *Part 3A: Dashboard Data Table TROUBLESHOOTING
The error “#REF” indicates that the reference cells for the formula are not found, but the good news is, it’s an easy fix!
Click on the Average Intensity for 410nm.
Type the following formula into the cell: =AVERAGE(TBL_HST[CH1])
Notes: Image Source (All) – Abbott (Self)

## Slide 27: DATA COLLECTION – *Part 3A: Dashboard Data Table TROUBLESHOOTING
4. Each cell formula going down the column should increase by 1 channel.
5. See the table to the right for the correct formulas for Average Intensity at each wavelength.
6. You can copy and paste the formulas for each wavelength from the next slide!
Notes: Image Source – Abbott (Self)

## Slide 28: DATA COLLECTION – *Part 3A: Dashboard Data Table TROUBLESHOOTING
Click on the text box to the right ,
Select all the text, then copy, and paste!
=AVERAGE(TBL_HST[CH1])
=AVERAGE(TBL_HST[CH2])
=AVERAGE(TBL_HST[CH3])
=AVERAGE(TBL_HST[CH4])
=AVERAGE(TBL_HST[CH5])
=AVERAGE(TBL_HST[CH6])
=AVERAGE(TBL_HST[CH7])
=AVERAGE(TBL_HST[CH8])
=AVERAGE(TBL_HST[CH9])
=AVERAGE(TBL_HST[CH10])
=AVERAGE(TBL_HST[CH11])
=AVERAGE(TBL_HST[CH12])
=AVERAGE(TBL_HST[CH13])
=AVERAGE(TBL_HST[CH14])
=AVERAGE(TBL_HST[CH15])
=AVERAGE(TBL_HST[CH16])
=AVERAGE(TBL_HST[CH17])
=AVERAGE(TBL_HST[CH18])

## Slide 29: DATA COLLECTION – Part 4: Start Data
4. On the Dashboard Sheet, select the substance name from the dropdown menu.
5. Click “Start Data” from the Data Streamer menu bar.
6. Click on the “Data Out” Sheet from the bottom menu.
Then type “GO” into cell A5 and hit Enter.
Notes: Image Source (All) – Abbott (Self)

## Slide 30: DATA COLLECTION – Part 5: Collect Data
Return to the Dashboard Sheet using the menu at the bottom of the screen. You should now see values in the data table for average intensity, a bar graph, and a line graph created for you.
Once the values have stabilized (~10 seconds), click “Stop Data” toward the top of the screen.
Notes: Image Source (All) – Abbott (Self)

## Slide 31: DATA COLLECTION – Part 6: Save Data
OPTION #1: Select “File,” then “Save As.”
Suggestion: Save files using the following pattern:
“ClassPeriod_Group#_SameName”
“ClassPeriod_GroupInitials_SameName”
e.g., “Hr1_ABC_TableSalt”
OPTION #2: Select “Capture Screen”
Within the Data Streamer menu is “capture screen”; this creates an image of the sheet shown that students can save.
OPTION #3: Use the “Print Screen” shortcut.
Using this keyboard shortcut does the same thing as screen capture above, but automatically saves the image to your “screenshots” folder.
Notes: Image Source (All) – Abbott (Self)

## Slide 32: DATA COLLECTION – Part 7: Record Data
Identify the wavelength values where “peaks” occur on the line graph (see left).
On the student worksheet, use a black marker to draw lines on the provided spectrum at each of the wavelengths where a peak occurred.
Notes: Image Source (All) – Abbott (Self)

## Slide 33: DATA COLLECTION – Part 8: Reset Data
1. Select the next substance to be sampled from the dropdown menu on the dashboard.
3. Press the reset button on the Arduino.
2. Click on the “Reset Data” icon under the data streamer menu.
Notes: Image Source (All) – Abbott (Self)

## Slide 34: DATA COLLECTION – Part 9: Repeat
Repeat the steps to collect data for each of the known samples and the unknown sample.
KNOWN A
KNOWN B
KNOWN C
UNKNOWN
(A/B/C)
Notes: Image Source (All) – Abbott (Self)

## Slide 35
4. Post Lab
Final steps of the lab activity are included in this section, including how to analyze the data collected and identify the unknown substance.

## Slide 36: DATA ANALYSIS
Once data and graphs are collected for the 3 known samples and 1 unknown, compare the unknown graph and spectrum to the knowns to identify the sample.
KNOWN A
KNOWN B
KNOWN C
UNKNOWN
MATCH!
Notes: Image Source (All) – Abbott (Self)

## Slide 37: COMPLETE STUDENT HANDOUT
After identifying their unknown substance, students should complete the analysis questions on the student handout.
KEY
Notes: Image Source (All) – Abbott (Self)

## Slide 38: Sources
Kramida, A., Ralchenko, Yu., Reader, J. and NIST ASD Team (2022). NIST Atomic Spectra Database (version 5.10), [Online]. Available: https://physics.nist.gov/asd. National Institute of Standards and Technology, Gaithersburg, MD. DOI: https://doi.org/10.18434/T4W30F
Seidle, Nathan (Nate). Spectral Triad (AS7265x) Hookup Guide, [Online]. Available: https://learn.sparkfun.com/tutorials/spectral-triad-as7265x-hookup-guide?_ga=2.208195537.274963032.1659022095-1771007873.1658366162. SparkFun Electronics. Licensed by CC BY-SA 4.0