## Slide 1
Much More Than Pretty Colors

## Slide 2
#f8a81b

## Slide 6
Have you ever thought about what makes a good food coloring?

## Slide 7
A good food coloring needs to be:
Soluble in water
Able to retain their color for a long time

## Slide 8
How is that possible?

## Slide 9
FD&C blue dye #1
Ionic compounds that dissolve in water are polar.

## Slide 10
Food dyes absorb and transmit a certain color
How much?
Absorbance and concentration are related

## Slide 11
Engineers use this relationship in quality control laboratories for food and pharmaceutical industries.

## Slide 12
Lab Connection: Measuring the absorbance of solutions with various concentrations of food dye and measure the concentration of a Gatorade sample.
Engineering: To design/construct a spectrophotometer/measuring instrument/analyzers
Today’s Activity

## Slide 13
Teacher Demonstration - Absorbance
Food dyes have molecules that absorb some wavelengths of light and let others pass through.
Absorption is caused by bringing an electron in a molecule, atom, or ion to a higher energy level.

## Slide 14
y=mx + b
b= 0= y intercept is zero
y= abc

## Slide 15
Spectroscopy is the study of the interaction of light and matter as a function of wavelength.
Engineers and scientists use spectroscopy as a tool to analyze the interaction between light and matter.

## Slide 16
Unknown Sample - Gatorade
Known Sample - Stock solution with blue food color

## Slide 17
What is the unit of concentration of a solution?
Molarity (M)

## Slide 18
Write the dilution formula
M1V1=M2V2

## Slide 19
M1= 6 x 10-6 (for all)
V2 = 10 ml (for all)
V1 from the data table
Substitute and calculate M2
M1V1=M2V2
6 x 10-6 x 2 = M2 x 10
M2 = (6 x 10-6 x 2)/10

## Slide 20
Test tube # | Volume of the stock solution (ml) V1 | Volume of water (ml) | Concentration of diluted sample (M) M1V1=M2V2
1 Blank | 0 | 10 | 0
2 | 2 | 8 | 1.2 x 10 -6
3 | 4 | 6 | 2.4 x 10-6
4 | 6 | 4 | 3.6 x 10-6
5 | 8 | 2 | 4.8 x 10 -6
Data Table
M1= 6 x 10-6 (for all) V2 = 10 ml (for all)
V1 (from the data table) Substitute and calculate M2

## Slide 21
Construct a spectrophotometer with the given popsicle sticks.
Make a sample holder that holds the sample, the detector and light source at an appropriate distance.

## Slide 22
Download ColorimeterX on your smartphone

## Slide 25
Procedure to measure absorbance:
Take 10 ml of the blank (distilled water) and wipe the side to make it clean and dry.
Tap the color identifier on your smartphone and record the red value on your data sheet.
Repeat steps 1-3 with diluted samples # 2-5.
Record the data in the data table in the appropriate concentration row.
Take a picture of your experimental setup and include it in your lab report.
Measure the absorbance of the unknown sample.

## Slide 26
Test tube | Stock Solution (6 x 10-6 M) | H2O (ml) | Concentration (M) | R value | Absorbance = -log(I/I0)
1 | 0 | 10 | 0.00 |  | 
2 | 2 | 8 |  |  | 
3 | 4 | 6 |  |  | 
4 | 6 | 4 |  |  | 
5 | 8 | 2 |  |  | 
6 | 10 | 0 | 6 x 10-6 |  | 
Data Table

## Slide 27
Plot a graph on Excel.
Graph the data concentration (x-axis) vs. absorbance (y-axis).
Provide an appropriate title and label x and y axes.
Enter the values of concentration and absorbance into two columns.
Highlight the cells and click on scatter plot.
Right click on the graph and click on Trend Line.
Then click on add equation and display equation. You will get an equation in y = mx +c format.
Select Linear as the Fit Equation  The best -fit linear regression line will be shown on the graph for your five data points.

## Slide 28
Additional Pictures of Experimental Set up