## Slide 1
Let’s Get Cracking! Force Sensor Instructions

## Slide 2
Quantity | Description | Price
1 | HX711 Amplifier (Weight Weighing Load Cell Conversion Module for Arduino Microcontroller) | $7.69
1 | Mustcam 5 Megapixel USB Digital Microscope with Measurement Software for Windows/Mac | $39.99
1 | 50 kg Platform Scale Sensor Weighting Sensor Load Cell Sensor for Electronic Balance | $13.99
1 | Adafruit Motor/Stepper/Servo Shield for Arduino v 2.3 Kit | $19.95
1 | Arduino UNO | $22.00
1 | 400mm Length Travel Linear Stage Actuator with Square Linear Rails + CBX1605 Ball Screw 1605 Ballscrew Motorized XY XYZ Linear Stage Table with Nema23 | $132.28
1 | Digi-Key AC/DC 3.3V 6.6W Power Supply | $13.47
 | TOTAL | $249.37
Force Sensor Parts List (prices accurate December 2019)

## Slide 3
TO STEPPER MOTOR
BLACK GND to GND
GREEN DT to A1
WHITE SCK to A0
RED VCC to 5V
TO DC BARREL JACK
50 KG LOAD CELL SENSOR
HX711 AMPLIFIER
NEMA23 STEPPER MOTOR ON RAILS
ADAFRUIT MOTOR SHIELD V2.3 MOUNTED TO ARDUINO UNO
AC/DC 3.3V 6.6W POWER SUPPLY
VIN JUMPER REMOVED
Force Sensor Wiring Diagram

## Slide 4
HX711 on PCB
Motor shield on Arduino UNO

## Slide 5
Motor shield on Arduino UNO

## Slide 6: The Software Side of Things…
Connect the Arduino UNO Board to your computer using the USB cable.
You will need to download and install two libraries (see https://www.arduino.cc/en/Guide/Libraries):
  Adafruit_Motor_Shield_V2_Library-master.zip
  HX711-master.zip
You will need to include them in the Arduino sketch.
Use the NoBonesAboutIt.ino code shown on the next page or write your own.
Check for compiling errors and then upload to the Arduino board.
Connect the power supply to the motor shield to power the motor.
Calibrate the scale using the procedure (in two pages).
After you set the scale calibration value in the code, you will need to re-compile NoBonesAboutIt.ino and upload to the Arduino board again.
Finally, open a Serial Window (newline) and type type U and D for up and down using the interleave stepping function or u and d to use the microsetepping function; in either case, you will be prompted to enter the number of steps. Type t for tare and m for measure.

## Slide 7
Sample Arduino Code

## Slide 8
Use Arduino to open the NoBonesAboutIt program.
Remove the scale.set_scale() number. You will replace it later at the end of this procedure.
Type t for tare. This is your (0, 0) starting point in the graph shown below.
Add known weights, beginning with a basket for holding weights and measure each successive force reading. I attached some embroidery floss to a plastic hummus cup as my basket.
After verifying that the results are linear, find the slope of the line. This is your scale factor.
Add the number to the scale.set_scale(79.1156) line and upload the updated code to the board.
REMOVE NUMBER FROM ()
Calibrating the Scale