## Slide 1
Oh Baby! Contractions and Calculations / Activity Part 3

## Slide 2: The Analog-to-Digital Converter The Arduino has a built-in analog to digital converter capable of storing a 10-bit number. Therefore, the Arduino can recognize 210 = 1024 different values ranging from 0‒1023.
1 | 0 | 1 | 1 | 0 | 1 | 1 | 1 | 1 | 1
Digital Value 735 |  |  |  |  |  |  |  |  | 

## Slide 3: The Delimeter Character In this activity, we are using serial communication to transmit data (FSR values) over Bluetooth. This means the Arduino sends each character as an 8-bit byte using the ASCII character value encoded as a decimal. The receiving end, the Android device, defaults to displaying byte values using the assigned ASCII value. Each force value (message) is separated by the decimal-encoded ASCII character for a line feed.

## Slide 4: ASCII Line Feed
Photos should be a
square like this.
ASCII table

## Slide 5: Buffers and Bytes Setting the number of bytes to receive = -1 (or any negative number), signifies that there is no maximum number of bytes to the serial message.

## Slide 6: Delimeters, Buffers, and Timing You will need a delay (1000 milliseconds) in the Arduino code and a clock timer (250 milliseconds) in the MIT App Inventor code. You want the app timer to be faster than the Arduino delay. If it were the other way around, then there would be a lag on the app end. The app would not be able to process the information because data would arrive faster than it can process it. But if the app is faster than the Arduino delay, then there will never be any bytes in the buffer.
App Clock Interval (ms) | < | Arduino Delay (ms)
 | < | 

## Slide 7: A Serial Packet or Frame Each character in a message has start and stop bits to indicate the beginning and end of the byte along with a parity bit (outside today’s scope) that basically checks for even/odd errors. We are concerned with the 8-bit byte of message. Let's say that we had two sensor values in a row, separated by the line feed character. Suppose the sensor values were ADC 57 followed by ADC 864. The way the serial communication works is to send the character 7 encoded for ASCII as a decimal, followed by the 5, followed by the line feed character code, followed by the 4, then 6 then 8, then finally the line feed.
Start Bit | Bit 7 | Bit 6 | Bit 5 | Bit 4 | Bit 3 | Bit 2 | Bit 1 | Bit 0 | Parity Bit | Stop Bit

## Slide 8: Two Readings and Two Delimeters Let’s look at the ASCII table and discuss the values in the table below.
ASCII Characters |  | 
Character | Decimal | Binary
7 | 55 | 0011 0111
5 | 53 | 0011 0101
LF | 10 | 0000 1010
4 | 52 | 0011 0100
6 | 54 | 0011 0110
8 | 56 | 0011 1000
LF | 10 | 0000 1010

## Slide 9: The Serial Flow
T
R
A
N
S
M
I
T
R
E
C
E
I
V
E
0 | 0 | 1 | 1 | 0 | 1 | 1 | 1
0 | 0 | 1 | 1 | 0 | 1 | 0 | 1
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
0 | 0 | 1 | 1 | 0 | 1 | 0 | 0
0 | 0 | 1 | 1 | 0 | 1 | 1 | 0
0 | 0 | 1 | 1 | 1 | 0 | 0 | 0
0 | 0 | 0 | 0 | 1 | 0 | 1 | 0
 | B | U | F | F | E | R | 
 | B | U | F | F | E | R |