## Slide 1
Analyze Brain Waves

## Slide 2: Brain Wave Review

## Slide 3: EEG, EKG, and EMG
We can measure the electrical activity of our nervous system, heart, and muscles using EEG, EKG, and EMG, respectively
  EEG stands for electroencephalogram, and it is used to measure brain waves
  EKG (or ECG) stands for electrocardiogram, and it is used to measure electrical signals in the heart muscle
  EMG stands for electromyogram, and it is used to measure electrical signals in the muscles
In this lecture, we will focus on EEG, and how we can analyze the measured waves

## Slide 4: Our Toolbox
Now that we know about the different types of brain waves, how do we take a brain wave dataset and determine which waves are present?
  We can use the following mathematical processes to “break down” a raw EEG signal and analyze it:
    Fast Fourier Transform (FFT)
    Power Spectral Density (PSD)
    Bandpass Filter

## Slide 5: Fast Fourier Transform (FFT)
Sinusoids observed in the real world are not “perfect,” but they can be modeled using combinations of sinusoids
  Example: The black signal below is modeled using a combination of the pink signals below it

## Slide 6: Fast Fourier Transform (FFT)
A Fast Fourier Transform (FFT) may be used to visualize the different frequencies of a signal’s component sinusoids
When we measure the raw EEG of a brain wave, we use the FFT to plot all the component frequencies observed in the wave
  Using the FFT output, we can see which frequencies are “dominant” (appear the most) in the raw signal
  If we notice that a frequency of ~ 1 Hz is dominant, we can conclude that the person is likely in a deep sleep since this frequency is representative of the delta wave
We won’t worry about the details of the FFT—just know what it’s used for!

## Slide 7: Fast Fourier Transform (FFT) Example

## Slide 8: Example of a Real-Time EEG with FFT
Notes: Make note of the FFT in the top right—this shows the distribution of frequencies (types of brain waves)

## Slide 9: Power Spectral Density (PSD)
The power spectral density (PSD) is the distribution of the signal’s power over the frequency
When we want to analyze which types of brain waves are dominant in a raw EEG signal, we can calculate and plot the PSD of the signal to visualize which waves “occur” most often in the signal

## Slide 10: Power Spectral Density (PSD) Example
In the example below, there are two peaks at f = 40 Hz and f = 75 Hz
  These peaks show us that most of the original signal’s power comes from waveforms with frequency 40 Hz and 75 Hz

## Slide 11: Bandpass Filter
A bandpass filter may be used to “filter out” parts of the original signal that are not within a range (or band) of specified frequencies
When we are analyzing an EEG signal, we can choose to only view wave components that are within the frequency range of a specific type of brain wave
  Example: We can choose the band 9 Hz – 13 Hz if we wish to view the alpha wave components

## Slide 12: Bandpass Filter

## Slide 13: Compare EEG Results
Notes: Note: Hypsarrhythmia is the term for a very chaotic and disorganized brain electrical activity with no recognizable pattern,
Optional: Have students compare other EEG results, such as: https://www.ncbi.nlm.nih.gov/books/NBK499867/figure/article-28842.image.f2/