## Slide 1: Maze Challenge
Notes: Maze Challenge activity > TeachEngineering.org
Image source: Microsoft clipart at http://office.microsoft.com/en-us/images/results.aspx?qu=maze&ex=1#ai:MC900299145|mt:1,2|

## Slide 2: Pre-Activity Quiz
What is a design challenge?
How do you program a robot to move 2 feet forward in a straight line?

## Slide 3: Pre-Activity Quiz Answers
What is a design challenge?
A design challenge starts with problem you want to solve. You think through the challenge logically and plan a design solution. Using suitable and available materials and following the steps in the engineering design process, you create, test and evaluate your best solution to the challenge. As necessary, you iterate (repeat) this process until a successful design is achieved.
How do you program a robot to move 2 feet forward in a straight line?
Calculate the distance that the robot moves forward for one motor rotation. Let’s say, it moves X inches with one motor rotation. Then divide 2 feet, which is 24 inches, by X, that is, calculate 24/X and program the motor to rotate 24/X.

## Slide 4: What Is a Design Challenge?
Day 1 - 50 minutes
In our modern world, challenges are everywhere!
How can we waste less? How can we harness solar energy and other renewable energy more effectively? How can improve transportation? How can we build roads and bridges? How can we design a house that is not too expensive? How can we build smarter cars? How can we use technology to make our cars safer?
These are big ideas that engineers and scientists work on to help improve the world we live in.
We will investigate how to complete a few design challenges through two different methods:
Creating different robot designs to help it better complete the challenges
Creating programs to help the robot complete the design challenge
Notes: Day 1: 50 minutes

## Slide 5: Your Engineering Challenge:
To build and program a robot to travel through a maze.
We will look at different robot designs (with and without sensors) in order to determine which is more reliable and which is faster.
Both the design of the robot and how it’s programmed are important for this challenge!

## Slide 6: Let’s Look at Some Basics
Before we start the design challenge, it is important to understand how and why we need to be careful with designing the robot and designing its program.
Also, it is very important that we understand how a robot follows instructions so we can understand how to program it.
Let’s do an activity to help us understand two important ideas:
  How a robot follows instructions
  The importance of sensors

## Slide 7: Let’s Look at Some Basics (continued)
It looks like this diagram 
Use tape (or boxes) to mark the boundaries shown in fine lines.
Blindfold a student “robot” and have him stand at the maze start.
Have a student “programmer” give a series of commands to instruct the “robot” to complete the maze without touching the maze edges (keeping hands at his/her sides).
6 ft
6 ft
3 ft
end
start
wall
wall
Command examples: go forward X steps, turn left, etc.
Maze 1 is a 3-ft wide path in a corner of the classroom.
Notes: Source of blindfolded boy image: Microsoft clipart: http://office.microsoft.com/en-us/images/results.aspx?qu=blindfolded&ex=1#ai:MC900347187|

## Slide 8: Let’s Look at Some Basics (continued)
What did you observe?
Did the “programmer” get the blindfolded “robot” through the maze?
Did the “commander” always tell the “robot” to go the correct number of steps?
Often, it is easier for the “programmer” to give instructions if s/he can tell the “robot” to go forward until s/he senses something
By doing it that way, the “programmer” does not have to worry about telling the “robot” exactly how many steps to move.

## Slide 9: Let’s Look at Some Basics (continued)
Choose a different volunteer “robot” to be blindfolded.
This time, permit the volunteer “robot” to stretch his/her hands out in front to sense when s/he is approaching a wall.
Have another student give commands to instruct the volunteer to get through the maze
6 ft
6 ft
3 ft
end
start
wall
wall
Now, commands such as “go forward until you sense a wall” are allowed.

## Slide 10: Let’s Look at Some Basics (continued)
What did you observe?
Was it easier to give instructions the first time or second time?
It is generally easier to tell a robot to go forward until it senses something (like a wall) than to tell it exactly how far it should go before turning. This approach also tends to be faster.
Notes: Images sources: (left) 2005 Tracee L. Jackson, U.S. Marine Corps via Wikimedia Commons http://commons.wikimedia.org/wiki/File:Blindfoldlowres.gif; (middle) GK-12 Program, Computational Neurobiology Center, College of Engineering, University of Missouri; (right) North Carolina State Parks http://www.ncparks.gov/Visit/parks/hari/pics/harp_maze.jpg

## Slide 11
What else did you observe?
Did you notice that the “commander” had to make sure to tell the “robot” EVERYTHING? …which direction to move, how far or how long to move, when to turn, which way to turn, etc.
Likewise, the LEGO MINDSTORMS NXT intelligent brick must be given exactly the same information. It knows nothing and will do exactly what you tell it to do. If you make a programming error, the robot will follow that incorrect command, and the fault is with the programmer, and not the robot!
Let’s Look at Some Basics (continued)

## Slide 12: Before you start…
Before we start our maze challenges, let’s learn the relationship between motor (or wheel) rotation and the corresponding distance the robot travels.
Why is this important? Because, when we have the robot travel the maze without any sensors, we must tell it how much distance to move.
Use your results from the Master Driver activity to inform your programming! (Recall that this is the activity where you determined the distance traveled by the taskbot for every rotation of the NXT motor.)

## Slide 13
Challenge 1: Make the LEGO robot navigate the maze without using any sensors
Challenge 2: Make the LEGO robot navigate the maze using the sound sensor, the touch sensor, and ultrasonic sensor at least once each
A Real Maze
Day 2 - 50 minutes

## Slide 14: The Challenges Maze
Suggested dimensions for the maze are shown in the diagram below, with “start” and “finish” locations indicated. 
Make the maze at least 1-ft high and 1.5-ft wide
7 ft
start
1 ft
4 ft
1 ft
finish
1.5 ft
Notes: Feel free to modify the maze dimensions as makes sense for your class.

## Slide 15: Challenge 1
To program the taskbot to travel the maze without using sensors.
For this first challenge, the robot must go through the maze without using sensors!
How will you program the robot to do this?
Think back to the Master Driver activity and what you learned about the relationship between the number of rotations of the motor and the distance the robot moved.
You will be provided with a measuring stick or tape measure for this challenge. Be resourceful!

## Slide 16: Challenge 2
To program the taskbot to travel the maze using the sound sensor, touch sensor, and ultrasonic sensor each at least once.
For this challenge, your robot must use the touch sensor, sound sensor and ultrasonic sensor at least once each when navigating the maze.
Think back to how we did basic programming with the touch sensor, ultrasonic sensor and sound sensor, and combine that information to get the robot to travel through the maze.
In the robot documentation, find information about attaching sensors to the robot. Or, come up with your own designs for attachment also for this challenge. Be creative!

## Slide 17: Post-Activity Quiz
What types of problems did you encounter when trying to complete the design challenges?
How did you change the design of your robot or your programs to help you complete the tasks?

## Slide 18: Post-Activity Quiz Answers
1. What types of problems did you encounter when trying to complete the design challenges?
  Calculating how many rotations to use in order to have the robot move a measured distance in the maze.
  Recalling how to begin programming; how to program each sensor.
2. How did you change the design of your robot or your programs to help you complete the tasks?
  We re-attached the sensors to position them correctly to receive the necessary input information.
  Through troubleshooting we corrected some programming errors.

## Slide 19: Maze without Sensors Solution
Recall the relation between rotations and distance: For each rotation, the robot travels a certain distance (inches or cms) and we can use multiplication to approximate how far the robot will travel.
So, we must measure each section of the maze and guess how many rotations we need based off each distance!
This may not work perfectly the first time, but the number of rotations can be modified so it eventually works.
Challenge 1

## Slide 20: Challenge 1 Program Solution
7 ft
start
1 ft
4 ft
1 ft
end
1.5 ft
2.5 ft
5.5 ft
4 ft
1.75 ft
In an effort to keep the robot as far from the walls as possible, calculate path distances so that the robot stays in the center of each corridor (.75 ft away from the wall).
1.75 ft

## Slide 21: Challenge 1 Program Solution (continued)
1
2
3
4

## Slide 22: Challenge 1 Program Solution (continued)
5
6
7
8

## Slide 23: Challenge 1 Program Solution (continued)
9
10
11
Note: Durations are approximate and may need to be adjusted differently for different robots.

## Slide 24: Maze Using Sensors Solution
How to complete the maze by using the LEGO robot sound, touch and ultrasonic sensors:
Remember, since we can use the sensors, we do not have to worry about distance and guessing how many rotations we need!
For each section of the maze, we can program the forward and backward movement blocks using unlimited, and then immediately place a sensor block after the movement block.
We must use the ultrasonic and sound sensor once in this program, then we can choose to use the sound sensor for the rest of the maze or the ultrasonic sensor for the rest of the maze or both.
Challenge 2

## Slide 25: Challenge 2 Program Solution
1
2
3
4

## Slide 26
5
6
7
8
Challenge 2 Program Solution (continued)

## Slide 27
9
10
11
12
Challenge 2 Program Solution (continued)

## Slide 28
13
14
15
16
Challenge 2 Program Solution (continued)

## Slide 29
17
18
19
20
Note: Block 20
is not strictly
necessary.
Challenge 2 Program Solution (continued)

## Slide 30: Vocabulary
design: Loosely stated, the art of creating something that does not exist.
engineering: The use of science and mathematics to solve problems to improve the world around us.
Notes: Image source: Microsoft clipart at http://office.microsoft.com/en-us/images/results.aspx?qu=maze&ex=1#ai:MC900299145|mt:1,2|