## Slide 1: Loops and Switches
Notes: How Do You Make Loops and Switches? lesson > TeachEngineering.org

## Slide 2
1. What kind of blocks are these?
2. Name two kinds of controls that can be specified to determine how long a loop repeats.
3. Give an example of a program you could write that would use a switch.
Loops and Switches Pre-Quiz

## Slide 3
1. What kind of blocks are these?
loop
switch
2. Name two kinds of controls that can be specified to determine how long a loop repeats.
  Any two of these: “Forever” (a never-ending loop), any sensor, “count” (tell the loop to repeat, for example, 5 times), “time” (tell the loop to repeat, for example, 1 minute), logic
3. Give an example of a program you could write that would use a switch.
  Example answer: While the touch sensor is pressed, go forward; otherwise, move backwards.
Loops and Switches Pre-Quiz Answers

## Slide 4
Objective
Loops and switches are two of the most important tools used in programming.
Loops allow us to repeat segments of a program indefinitely or until some condition is met
Switches allow a program to respond differently to different conditions
In today’s lesson, we:
Investigate how loops and switches work
Learn how to use loops and switches when we program using the LEGO MINDSTORMS NXT software
Learn to use switches and loops in unison to expand the functions of the programs we will make
What are loops and switches?
(50 minutes)

## Slide 5
In programming, a loop is an operator that allows us to repeat a set of commands indefinitely.
In many factories, a machine performs the same simple task thousands of times in a day
Watch a video clip of an assembly machine www.youtube.com/watch?v=AwJflkd6Y_o (1:41 minutes)
As a programmer, you don’t want to have to copy instructions for repeating that same simple task thousands of times…
So, instead, you write commands for the simple task once, and then enclose those commands in a loop, which can be repeated as many times as you want.
Loops: What Are They?

## Slide 6
Suppose we want to make a robot move once around in a square.
A program to do that has 8 blocks and would look like this:
start/stop at this corner 
Programming with Loops

## Slide 7
So. what we really want to program is simply:
Repeat (1. go forward; 2. turn right) 4 times.
In the LEGOMINDSTORMS NXT software, the loop block icon looks like this 
Drag this block down to the main line of your program as shown:
Notice that the 8 commands we would use to do this (forward, right, forward, right, forward, right, forward, right) are really just the same 2 commands repeated 4 times
Programming with Loops (continued)
Programming this task becomes a lot easier if you use “loops.”

## Slide 8
When you highlight the loop block, notice the drop-down menu next to “Control.”
The Control options enable you to tell a robot how long to keep looping the commands inside the loop.
Selecting “Forever” repeats those commands indefinitely.
Selecting “Sensor” repeats those commands until a sensor detects a stimulus (for example, until the touch sensor is pressed).
Selecting “Time” repeats those commands until a certain amount of time has expired (for example, 5 minutes).
Programming with Loops (continued)

## Slide 9
Selecting “Count” repeats those commands some specific number of times.
We won’t discuss selecting “Logic” at this time, because it is a bit too complicated for our application.
In this case, what do we choose? Since we want the commands (go forward, turn right) to be repeated 4 times, we select “Count” and set “count” to 4.
Programming with Loops (continued)

## Slide 10
Next, we need to drag the commands we want to be repeated INSIDE the loop.
The final program looks like this: 
Notice that instead of 8 blocks, we only need 2 blocks, surrounded by a loop.
Programming with Loops (continued)

## Slide 11
Do This:
Fill out Part 2 of the worksheet.
Then program the robot to:
Go forward until it hits a wall, then back up one rotation and turn left
Repeat these instructions until detecting a sound
Then stop
Mini-Activity 1

## Slide 12
1
2
3
Mini-Activity 1 Programming Solution

## Slide 13
4
5
6
(continued)
Mini-Activity 1 Programming Solution

## Slide 14
In programming, a switch is an object that gives different commands depending on which state it is in.
A light switch for example, has 2 states: up and down.
When the light switch is in the “up” position, the switch directs the light it controls to turn on.
When the light switch is in the “down” position, the switch directs the light it controls to turn off.
Day 2: What Is a Switch?

## Slide 15
Suppose we want to program a robot to end up exactly 24 inches from a wall no matter where it starts.
This means that the robot will always be in one of two states:
  closer than 24 inches to the wall
  or
  farther than 24 inches from the wall
We can best deal with this situation by using a switch.
To do this, click on the switch icon: and drag it down to the program line.
Programming with Switches

## Slide 16
When you highlight the switch block, notice that you can indicate the sensor used.
In this case, we are interested in how far away the robot is from the wall, so we select the ultrasonic sensor from the drop-down menu.
Because we want the state of the switch to depend on the distance the robot is initially away from the wall, we also need to set the distance to 24 inches.
Programming with Switches (continued)

## Slide 17
If the condition specified is satisfied, the program will execute the commands in the top half of the switch.
This means the robot is less than 24 inches from the wall and we need the robot to back up until it is at least 24 inches away from the wall.
We can achieve this by using a backward move block with unlimited duration followed by a wait block as shown below.
Programming with Switches (continued)

## Slide 18
If the condition specified is not satisfied, the program will execute the commands in the bottom half of the switch.
This means the robot is more than 24 inches from the wall and we need the robot to go forward until it is closer than 24 inches from the wall.
We can achieve this by using a forward move block with unlimited duration followed by a wait block as shown below.
Programming with Switches (continued)

## Slide 19
Do This:
In worksheet Part 3, write out the program we just discussed in WORDS, that is, as an algorithm, and understand it fully.
Then, write the NXT program, download it onto the LEGO taskbot and verify that it works correctly.
Note that all the blocks for this program are provided on the previous slides.
Mini-Activity 2

## Slide 20
Mini-Activity 2 Programming Solution

## Slide 21
Do This:
Program the robot so that:
It moves forward until it hears a sound.
If the touch sensor is pressed when it hears a sound, turn left.
If the touch sensor is not pressed when it hears a sound, turn right.
Mini-Activity 3

## Slide 22
1
2
3
Programming Activity Solution

## Slide 23
4
5
Programming Activity Solution (continued)

## Slide 24
1. What kind of blocks are these?
2. Name two kinds of controls that can be specified to determine how long a loop repeats.
3. Give an example of a program you could write that would use a switch.
Loops and Switches Post-Quiz

## Slide 25
1. What kind of blocks are these?
loop
switch
2. Name two kinds of controls that can be specified to determine how long a loop repeats.
  Any two of these: “Forever” (a never-ending loop), any sensor, “count” (tell the loop to repeat, for example, 5 times), “time” (tell the loop to repeat, for example, 1 minute), logic
3. Give an example of a program you could write that would use a switch.
  Example answer: While the touch sensor is pressed, go forward otherwise move backwards.
Loops and Switches Post-Quiz Answers

## Slide 26
loop: A command or “operator” that repeats a set of commands.
switch: In programming, an object that gives different commands depending on which state it is in.
Vocabulary

## Slide 27
Slide 1: girl on floor with laptop; source: Microsoft® clipart: http://office.microsoft.com/en-us/images/results.aspx?qu=laptop&ex=1#ai:MP900442369|
Slide 1: multicolored chevron loop; source: Microsoft® clipart: http://office.microsoft.com/en-us/images/results.aspx?qu=cycle&ex=1#ai:MC910216324|
Slides 1, 14: wall switch drawing; source: Microsoft® clipart: http://office.microsoft.com/en-us/images/results.aspx?qu=light+switch&ex=1#ai:MC900441745|
Device and programming images from LEGO MINDSTORM NXT User’s Guide http://goo.gl/wuhSUA
Screen captures and diagrams by author
Images Sources