## Slide 1
Investigating Ideal and Actual Mechanical Advantage

## Slide 2: Ideal Mechanical Advantage Ideal Mechanical Advantage (IMA) is an excellent way to get an apples-to-apples comparison of “theoretical” mechanical advantage between two structures. However, it does not account for friction.
IMA calculation:
Resistance Distance
--------------- Effort Distance

## Slide 3: Ideal Mechanical Advantage In this example, the resistance distance (dR) is 10 meters, and the effort distance (dE) is 25 meters.
Resistance Distance
--------------------------- = IMA
Effort Distance
10m
------- = 0.4
25m

## Slide 4: Ideal Mechanical Advantage Now you try!
IMA calculation:
Resistance Distance
--------------- Effort Distance
dR _______
----------- = IMA ______
dE _______
dR _______
----------- = IMA ______
dE _______

## Slide 5: Ideal Mechanical Advantage Were you right?
IMA calculation:
Resistance Distance
--------------- Effort Distance
dR 3m
----------- = IMA 0.11
dE 28m
dR 100m
----------- = IMA 0.74
dE 135m

## Slide 6: Actual Mechanical Advantage Actual Mechanical Advantage (AMA) is similar in nature to IMA, but we are now considering the forces of friction in both the weight (resistance force) of the object and distance traveled (effort force) so we can get a more realistic feel. We call these “forces,” measure them in Newtons (N) using a spring scale, and label them as RF for resistance force and FE for effort force.
Newtons can easily be converted to units of weight. For example, 1 kg is equal to approximately 9.8 Newtons. Google has a converter built into its calculators.
AMA calculation:
Resistance Force
--------------- Effort Force

## Slide 7: Actual Mechanical Advantage In this example, the Resistance Force RF is 50N as measured by the scale, and the Effort Force FE is 5N as measured by dragging the weight over the inclined plane.
Resistance Force
--------------------------- = AMA
Effort Force
50N
------- = AMA 10
5N
We can say that this inclined plane makes the work 10 times easier!

## Slide 8: Actual Mechanical Advantage Now you try!
AMA calculation:
Resistance Force
--------------- Effort Force
RF _______
----------- = AMA ______
FE _______
RF _______
----------- = AMA ______
FE _______

## Slide 9: Actual Mechanical Advantage Were you right?
AMA calculation:
Resistance Force
--------------- Effort Force
RF 35N
----------- = AMA 3.5
FE 10N
RF 100N
----------- = AMA 3.57
FE 28N
Which one is easier?