## Slide 1
Scrub the Scum, Save the Shine – Prototype Testing Procedure

## Slide 2: Your goal: Create a motor-driven brush that: (1) Maximizes the ability to shine/clean a surface. (2) Minimizes wear on the surface. This is how you will test to see whether your prototype accomplishes your engineering design goals.

## Slide 3
Individual Prototype Testing

## Slide 4: Gather materials: - 4 metal “coins” - 1 piece of solid cardboard - double-sided tape - 1 dry erase marker - timer - Prototype Testing worksheet - your prototype  Find a clear, dry, space to work.
Test 1: Scrub the Scum

## Slide 5: Test 1: Scrub the Scum Step 1: Attach your four coins to the cardboard by placing a small piece of double-sided tape on the back of each coin.

## Slide 6: Test 1: Scrub the Scum Step 2: Carefully use the dry erase marker to completely cover the top surface of each coin. This marker cover is what your prototype will clean off the coin during the test.

## Slide 7: Test 1: Scrub the Scum Step 3: Place your prototype on top of one of the coins. Use your fingers to make a barrier on the edge of the coin so the prototype will not fall off when turned on. NOTE: Do NOT press down on your prototype. The only force should come from the motor acting.

## Slide 8: Test 1: Scrub the Scum Step 4: Start the timer at the same time you turn on your prototype by attaching the motor to the battery. NOTE: You will be timing your prototype as it acts for 2 minutes on one coin. Do not press down on your prototype!

## Slide 9: Test 1: Scrub the Scum Step 5: After 2 minutes, turn off your prototype by detaching the battery from the motor. Remove your prototype from the coin surface.

## Slide 10: Test 1: Scrub the Scum Step 6: Evaluate how well your prototype cleaned the coin by comparing the appearance of the coin with the pictures on your testing evaluation guide:

## Slide 11: Test 1: Scrub the Scum Step 7: Record your data on your prototype testing worksheet. Repeat Steps 3 – 7 for the remaining coins.

## Slide 12
Group Prototype Testing

## Slide 13: Assign Group Roles
Materials Manager
Gather & return supplies, set up equipment, and use fingers to keep bot in place for testing.
Data
Recorder
Observe and record test data on worksheet.
Measurement
Guru
Start and stop the timer to ensure accuracy in testing; collaborate with team for measurements.
Electrician
Connect and disconnect the battery to start and stop the motor.

## Slide 14: Gather materials: - 4 metal “coins” - 1 piece of solid cardboard - double-sided tape - 1 dry erase marker - timer - Prototype Testing worksheet - your prototype  Find a clear, dry, space to work.
Test 1: Scrub the Scum

## Slide 15: Test 1: Scrub the Scum Step 1: Attach your four coins to the cardboard by placing a small piece of double-sided tape on the back of each coin.

## Slide 16: Test 1: Scrub the Scum Step 2: Carefully use the dry erase marker to completely cover the top surface of each coin. This marker cover is what your prototype will clean off the coin during the test.

## Slide 17: Test 1: Scrub the Scum Step 3: Place your prototype on top of one of the coins. Use your fingers to make a barrier on the edge of the coin so the prototype will not fall off when turned on. NOTE: Do NOT press down on your prototype. The only force should come from the motor acting.

## Slide 18: Test 1: Scrub the Scum Step 4: Start the timer at the same time you turn on your prototype by attaching the motor to the battery. NOTE: You will be timing your prototype as it acts for 2 minutes on one coin. Do not press down on your prototype!

## Slide 19: Test 1: Scrub the Scum Step 5: After 2 minutes, turn off your prototype by detaching the battery from the motor. Remove your prototype from the coin surface.

## Slide 20: Test 1: Scrub the Scum Step 6: Evaluate how well your prototype cleaned the coin by comparing the appearance of the coin with the pictures on your testing evaluation guide:

## Slide 21: Test 1: Scrub the Scum Step 7: Record your data on your prototype testing worksheet. Repeat Steps 3 – 7 for the remaining coins.

## Slide 22: Gather materials: - 4 metal “coins” - 1 piece of solid cardboard - double-sided tape - 1 dry erase marker - timer - Prototype Testing worksheet - your prototype  Find a clear, dry, space to work.
Test 2: Save the Shine

## Slide 23: Test 2: Save the Shine Step 1: Carefully remove the outer foil layer from one of the coins.

## Slide 24: Test 2: Save the Shine Step 2: Carefully measure the thickness of the coin with the cover removed by using the ruler or calipers. Record the original thickness in the data table on your prototype testing worksheet.

## Slide 25: Test 2: Save the Shine Step 3: Carefully place the coin into one of the slots in your coin holder OR, if using cardboard, place a piece of double-sided tape on the foil-covered side of your coin and attach the foil side to the cardboard so the uncovered side is facing up.

## Slide 26: Test 2: Save the Shine Step 4: Place your prototype on top of the coin that has the foil cover removed. Use your fingers to make a barrier on the edge of the coin so the prototype will not fall off when turned on. NOTE: Do NOT press down on your prototype. The only force should come from the motor acting.

## Slide 27: Test 2: Save the Shine Step 5: Start the timer at the same time you turn on your prototype by attaching the motor to the battery. NOTE: You will be timing your prototype as it acts for 2 minutes on one coin. Do not press down on your prototype!

## Slide 28: Test 2: Save the Shine Step 6: After 2 minutes, turn off your prototype by detaching the battery from the motor. Remove your prototype from the coin surface.

## Slide 29: Test 2: Save the Shine Step 7: Carefully remove the coin from the holder. Suggestion: Use the palm of your hand to cover any coins that remain in the holder and turn the holder over to dump the coin you just used for the test onto a flat surface.

## Slide 30: Test 2: Save the Shine Step 8: Use the ruler or calipers to measure the thickness of the coin in millimeters. NOTE: If the thickness varies at different points of the coin, estimate the thickness at the most worn (i.e., thinnest) point.

## Slide 31: Test 2: Save the Shine Step 9: Repeat Steps 1- 8 for the remaining coins.