## Slide 1: Testing Apparatus Construction
Step-by-Step Instructions
Notes: Testing Apparatus Construction Step-by-Step Instructions, Lab Research to Engineer a Phosphorescent Bioplastic activity, TeachEngineering.org
///
Source of all images: 2016 RET Program, School of Polymers and High Performance Materials, University of Southern Mississippi

## Slide 2
Get a 28.8 cm x 20.3 cm x 12 cm box
Assemble the box by folding it

## Slide 3: Tape the bottom and sides of the box

## Slide 4: Tape down the bottom flaps on the inside

## Slide 5: Tape the top and sides of the box

## Slide 6: Make sure all the sides are covered with tape to keep out ambient light

## Slide 7: Cut a circle the size of a petri dish Place this template on the top of the box

## Slide 8: Use a clamp and ring stand to secure a UV flashlight upright in the center of the template

## Slide 9: Place the light sensor probe (also secured upright by using a clamp and ring stand) next to the UV flashlight on the round template

## Slide 10: Remove the round template and trace the ends of the UV flashlight and light probe on the top of the box

## Slide 11: Notice the traced shapes below 

## Slide 12: Use a box cutter to carefully cut out the traced circles

## Slide 13: Sketch a door on the side of the box, away from the cut holes See the next slide for exact door size and location 

## Slide 14: Door location and dimensions
Locate the door 1 cm from the top of the box
Make the top and bottom sides of the door 14 cm long
Make the right side of the door 10 cm side
Locate the bottom of the door 2 cm from the bottom of the box

## Slide 15: Tape the door edges so when it is closed it keeps out ambient light and is easier to open between samples

## Slide 16: Open the door and tape down the top flaps on the inside of the box

## Slide 17: Under the UV light and light probe holes, tape down the round petri dish template to help with sample placement

## Slide 18
Use a ring stand and clamps to put the UV flashlight and light sensor probe into place
Place the light probe close to the sample, yet far enough away so that petri dish samples can be exchanged without disturbing the light probe

## Slide 19: Quantitative Analysis Instructions
Turn on the LabQuest and light probe
Set a timer for 2 minutes
Put a testing sample in place in the testing apparatus
Close the door (to shut out ambient light)
Turn on the UV flashlight
After 2 minutes, turn off the UV light and quickly record the first 5 numbers from the light probe and LabQuest
Average the 5 readings to get 1 quantitative measurement of the bioplastic’s phosphorescent glow
~ the testing process~

## Slide 20: Lab Quest reading of UV flashlight

## Slide 21: Lab Quest reading of UV flashlight

## Slide 22: Lab Quest reading after the UV light is turned OFF, so the reading is the glow of the plastic

## Slide 23: Reading while door is still closed