## Slide 1: Testing Apparatus Construction

## Slide 2: Assemble a box measuring approximately 29.8 cm x 20.3 cm x 12 cm

## Slide 3: Tape the bottom and sides of the box

## Slide 4: Tape down the bottom flaps on the inside of the box

## Slide 5: Tape the top and sides of the box

## Slide 6: Make sure all the sides are covered with tape to keep out ambient light

## Slide 7: Cut a circle the size of petri dish; place this template on the top of the box

## Slide 8: Secure the UV flashlight using a clamp and ring stand in the center of the template

## Slide 9: Secure the light sensor probe using the other clamp and ring stand next the UV flashlight and on the template

## Slide 10: Remove the template and trace around the ends of the UV flashlight and light probe on the top of the box

## Slide 11: Your tracing should look like this:

## Slide 12: Cut out the circles using a box cutter

## Slide 13: Trace a door on the side of the box away from the cut holes

## Slide 14: Cut out the door starting 1 cm from the top; the top and bottom sides of the door are 14 cm and the door is 10 cm wide; the bottom of the door is 2 cm from the bottom of the box

## Slide 15: Tape the edges of the door so when the door is closed it will keep out ambient light; it will also be easier to open between samples

## Slide 16: Open the door and tape down the top flaps on the inside of the box

## Slide 17: Under the UV flashlight and light probe holes, tape down the petri dish template for sample placement.

## Slide 18: Put the UV flashlight and light sensor probe into place using the ring stand and clamps; the light probe needs to be close to the sample but far away so that samples can be switched without disturbing the probe

## Slide 19: Directions for Quantitative Analysis
Make sure the LabQuest and light probe are turned on
Set a timer for 2 minutes
Put a test sample into place
Close door; record initial data reading
Turn on UV Flashlight
After 2 minutes, turn the UV flashlight off and record the first 5 readings of the LabQuest.
Average the 5 numbers for 1 quantitative reading; subtract the average from initial data reading to get a final quantitative data point

## Slide 20: LabQuest Reading of UV Flashlight

## Slide 21: LabQuest Reading of UV Flashlight

## Slide 22: LabQuest reading after the UV flashlight is turned off; the light sensor is picking up a reading from the glow of the sample

## Slide 23: Door is still closed