## Slide 1: A Robotic Hand with a Gentle Touch! Understand the Challenge
Notes: Day 1 Presentation
A Robotic Hand with a Gentle Touch Activity > TeachEngineering.org
Image source: http://www.nasa.gov/content/a-step-up-for-nasa-s-robonaut-ready-for-climbing-legs/#

## Slide 2: Outline
Curve fitting
Electrical engineering fundamentals
Curve modeling equations
Curve modeling graphs
Regression and correlation
Curve fitting with linear models
Finding best fit line using summation
Finding best fit line using calculator
Rise to the challenge
Notes: Preview of presentation topics covered in this presentation.

## Slide 3: Curve Fitting
The process of constructing a curve model, or mathematical function, that has the best fit to a series of data points.
Studying these models gives us a better understanding of the behavior and relationships among variables.
Curve models are an effective and efficient method to simulate solutions to real-world problems.
Curve modeling plays an important role in the electrical engineering field.

## Slide 4: Electrical Engineering Fundamentals
Current (I)
  A flow of electrical charge
Resistor (R)
  A passive two-terminal electronic component that implements electrical resistance as a circuit element
Voltage (V)
  The electric potential energy difference between 2 points.
Ground
  A reference point in an electrical circuit from which other voltages are measured
I = V/R
Show Ohm’s law simulation
Notes: To design cool inventions and make them work, electrical engineers deal with measurable quantities. These are the most basic units measured and used by electrical engineers. Students (and engineers) need to know these terms when reading about and designing electric circuits. Notice the symbols. Notice the equation (the relationship among the values).
Use a water analogy to explain the relationship between voltage (water pump), resistance (pipe size) and current (pressure meter).
As a class, experiment with KGBH’s Ohm’s Law Simulation at http://www.pbslearningmedia.org/asset/hew06_int_ohmslaw/; use the sliders to adjust the voltage and resistance in a circuit to observe this affects the flow of current according to Ohm’s law.

## Slide 5: Curve Modeling Equations
Ohm’s law: The current through a conductor between 2 points is directly proportional to the potential difference across the 2 points.
Newton’s second law of motion: The acceleration of a body is directly proportional to, and in the same direction as, the net force acting on the body, and inversely proportional to its mass.
Amdahl’s law: The maximum expected improvement to an overall system when only part of the system is improved.
Notes: Show students current and relevant curve models used by electrical engineers, physicists and computer engineers.

## Slide 6: Curve Fitting Graphs
Ohm’s law Amdahl’s law Newton’s second law
Notes: This slide shows example values of each equation. The blue line is the line of best fit for each set of points. When using the given equations, student only generate points on the blue line. This slide also serves as a visual for students who are visual learners.

## Slide 7: Regression and Correlation
Regression is the study of the relationship between variables.
Correlation is the strength and direction of the linear relationship between the 2 variables.
Notes: Demonstrate the different types of correlations. The left graph shows a strongly correlated relationship. The right graph shows no correlation. Throughout the year, student will study the relationships between two or more variables.

## Slide 8: Curve Fitting with Linear Models
A line of best fit is the line that comes closest to all data samples in a regression study.
A residual is the signed vertical distance between a data point and a line of fit.
Notes: This graph shows a strong correlation between test scores and the number of hours a person studies. Using a data set for this relationship, we are able to find a line of best fit. The line in blue is the line of best fit.

## Slide 9: Finding Best Fit Line Using Summation
You can find the best fit line by finding the sum of the squares of the residuals.
The sum with a value closest to 1 is the best fit line.
Notes: Demonstrate that a line of best fit has a summation with a value closest to 1.
The left graph shows a good best fit line where residuals are closer to it.
The right graph shows an inaccurate best fit line.

## Slide 10: Finding Best Fit Line Using Summation
The sum with a value closest to 1 is the best fit line.
Notes: This slide demonstrates the calculation and accuracy of each best fit line.

## Slide 11: Finding Best Fit Line Using Calculator
Using a TI-8X graphing calculator:
Press STAT and select EDIT.
Enter data into L1 and L2 using arrows.
Press STAT again and choose CALC.
Choose LinReg(ax+b) and press ENTER twice.
Notes: As necessary, adjust the instructions/steps to match the available technology students will use.
Image source: Microsoft clipart http://office.microsoft.com/en-us/images/results.aspx?qu=calculator&ex=1#ai:MC900384046|mt:1|

## Slide 12: Understand the Challenge
Welcome to Johnson Space Center, young NASA/GM engineers. It is with great privilege that I reveal to you our latest project—Robo-Glove!
Our latest prototype is functional, but not calibrated correctly. Our Robo-Glove used on Robonaut 2 keeps CRUSHING people’s hands when shaking them.
To improve our design, we would like you to add the revolutionary FlexiForce sensors on our Robo-Glove X2. Your task is to develop a working prototype of our glove, calibrate it using weights, and test it using an egg within three days!! If time allows, test it by shaking people’s hands.
Oh, one more thing, our senior electrical engineers do not want to replicate the calibration or testing. So please provide them with:
A scatterplot graph using resistance vs. force, conductance vs. force, and voltage vs. force (lbs)
And, for the last two graphs, create a best fit line on the graph and a best fit equation.
Notes: Explain to the class the activity’s engineering design challenge.
The aim of this real-world engineering project, the Robo-Glove, is to help astronauts and autoworkers reduce the risk of job-related repetitive stress injuries. The invention comes as a result of another NASA/GM creation, the Robonaut 2, a project that launched the first humanoid robot into space in 2011 and now resides on the International Space Station. Robonaut 2 is able to handily manipulate tools that were designed to be used by human hands. Through the use of sensors, actuators, and tendons that closely resembled nerves and muscles in the human hand, engineers created an uncanny level of hand dexterity with Robonaut 2.
Source of Robo-Glove and Robonaut 2 information and image: NASA http://www.webpronews.com/robo-glove-the-real-life-power-glove-from-space-2012-03

## Slide 13: References
Robots shaking hands (image) http://www.nasa.gov/images/content/471146main_jsc2010e089924_hi.jpg
KBGH’s Ohm’s law simulation http://www.teachersdomain.org/asset/hew06_int_ohmslaw/
GM News article: GM, NASA Jointly Developing Robotic Gloves for Human Use Robonaut technology coming to the factory floor or space station soon http://media.gm.com/media/us/en/gm/news.detail.html/content/Pages/news/us/en/2012/Mar/0313_roboglove.html
WebProNews article: Robo-Glove: The Real-Life Power Glove From Space Vulcan nerve pinches were never easier to perform. http://www.webpronews.com/robo-glove-the-real-life-power-glove-from-space-2012-03
Merriam-Webster Dictionary (source of definitions) http://www.merriam-webster.com/dictionary